## Slide 1: Measuring Forested Riparian Buffer Width with Lidar
A statistical comparison of 1m Lidar data against 1m state land cover data

## Slide 2: Background
Forested riparian buffers provide essential ecosystem services such as:
Bank stabilization
Water temperature control
Nitrogen & sediment removal
Flood mitigation
Wildlife habitat
http://www.dnr.state.md.us/forests/publications/sink.html
(Boesch & Greer, 2003)

## Slide 3: Background
Watershed monitoring programs require accurate information on land cover and land use change. (Goetz et al., 2004)
30m satellite data lacks the spatial resolution to assess FRB structure at critical scales. (Goetz et al., 2003)
1m IKONOS imagery and aerial photography have provided better results, but are economically prohibitive. (Goetz 2006. Lattin et al., 2004.)
http://www.mda.state.mn.us/protecting/conservation/practices/bufferforested.aspx
30m x 30m
1m x 1m

## Slide 4: Background
LiDAR has been proven effective for mapping forest canopy cover and height at 1m scales (Dubayah & Drake, 2000).
Growing popularity has led to many states acquiring LiDAR data, allowing it to be a cost-effective method data set to use for mapping FRB width (Goetz 2006).
http://lidarcomm.com/id28.html

## Slide 5
1. How does an assessment of Forested Riparian Buffer width differ between:
  a) LiDAR derived canopy cover maps
  b) State land use/land cover maps (based on aerial photography and human interpretation)
2. How is Forested Riparian Buffer width affected by adjoining land use type?
  Does this vary significantly depending on the method used to determine buffer width?
Research Questions

## Slide 6
Antietam Creek, Washington County, Maryland
Study Area
Largely rural in nature, but…
Much nearby agriculture leading to sediment and nutrient run-off
Urban run-off from expanding Hagerstown region

## Slide 7
Antietam Creek, Washington County, Maryland
Study Area
Largely rural in nature, but…
Much nearby agriculture leading to sediment and nutrient run-off
Urban run-off from expanding Hagerstown region
Developed
Agriculture
Forested

## Slide 8
1m LiDAR derived canopy cover map
Data/Methods
Canopy Cover
(Dubayah et al., 2012)
(Maryland Department of Planning, 2010)
2010 land use/land cover feature map
Developed
Agriculture
Forested
Simplified to 3 land use/land cover types.
Rasterized in ArcMap at 1m resolution.
Antietam Creek Shapefile:
Derived from Open Street Map database.
Much more accurate than national or state level databases.

## Slide 9
Methods
Transect layout following Wasser et al., 2015.
Developed
Agriculture
Forested
State LULC:
LiDAR Canopy Cover:
Forested
Transects:
10m x 10m windows
200m on either side
100m apart
1354 transects total
Calculated FRB

## Slide 10
1. How does buffer width calculation differ between input data sets?
Results
 | Lidar | State AP
Mean | 91.87m | 85.17m
Standard Deviation | 70.42m | 80.95m

## Slide 11
2. How is FRB width affected by adjoining land use type (per input data)?
Results
 | Agriculture | Developed | Forest
Mean (Lidar) | 60.48m | 74.88m | 70.73m
Mean (State AP) | 51.92m | 35.75m | NA
SD (Lidar) | 48.65m | 49.54m | 57.84m
SD (State AP) | 55.55m | 46.02m | NA

## Slide 12
Discussion/Conclusion

## Slide 13
References
Boesch D.F. and J. Greer (Editors), 2003. Chesapeake Futures: Choices for the 21st Century. Science and Technical Advisory Committee, Report 03-001 Chesapeake Research Consortium, Edgewater Maryland.
Dubayah, Ralph O., J.B.Drake. 2000. Lidar Remote Sensing for Forestry. Journal of Forestry.
Goetz, Scott J., R.K. Wright, A.J. Smith, E. Zinecker, E. Schaub. 2003. IKONOS imagery for resource management: Tree cover, impervious surfaces, and riparian buffer analyses in the mid-Atlantic region. Remote Sensing of the Environment.
Goetz, Scott J., C.A. Jantz, S.D. Prince, A.J. Smith, D.Varlyguin, R.K.Wright. 2004. Integrated Analysis of Ecosystem Interactions With Land Use Change: The Chesapeake Bay Watershed. Ecosystems and Land Use Change, Geophysical Monograph Series.
Goetz, Scott J. 2006. Remote Sensing of Riparian Buffers: Past Progress and Future Prospects. Journal of the American Water Resources Association.
Lattin, Peter D., P.J.Wigington, Jr., T.J.Moser, B.E.Peniston, D.R.Lindeman, D.R. Oetter. 2004. Influence of Remote Sensing Imagery Source on Quantification of Riparian Land Cover/Land Use. Journal of the American Water Resources Association.
Maryland Department of Planning. 2010. Land Use/ Land Cover for Maryland. http://planning.maryland.gov/OurWork/landUse.shtml
Wasser, Leah, L. Chasmer, R.Day, A.Taylor. 2015. Quantifying land use effects on forested riparian buffer vegetation structure using LiDAR data. Ecosphere.